## Slide 1
SIGCOMM’16
Tutorial
Jeongkeun “JK” Lee, Chang Kim
Aug 2016
Programming The Network Data Plane in P4

## Slide 2: P4 Introduction

## Slide 3: Status Quo: Bottom-up design
Networking App / Switch OS
Run-time API
Driver
“This is how I know to
process packets”
(i.e. the ASIC datasheet
makes the rules)
Fixed-function ASIC
?
Custom requirements
from your network

## Slide 4: A Better Approach: Top-down design
Networking App / Switch OS
Run-time API
Driver
“This is how I want the network to behave and how to switch packets…”
(the user / controller
makes the rules)
P4 Programmable Device
Custom requirements
from your network
P4

## Slide 5: Programmable Network Devices
PISA: Flexible Match+Action ASICs
  Intel Flexpipe, Cisco Doppler, Cavium (Xpliant), Barefoot Tofino, …
NPU
  EZchip, Netronome, …
CPU
  Open Vswitch, eBPF, DPDK, VPP...
FPGA
  Xilinx, Altera, ...
These devices let us tell them how to process packets.
Notes: These types of switch have their place: e.g. Hypervisor switches, rack switches, enterprise switches, edge routers, etc.

## Slide 6: Why we call it Protocol Independent Packet Processing

## Slide 7: Protocol-Independent Switch Architecture (PISA)
Switch Pipeline
Programmable
Parser
Match
Memory
Action
ALU
Notes: So, let me give you quick overview of the PISA design.
Programmable parser. Packets run from left to right, going through each stage. Each stage offers generic, protocol-independent match-action units. You can use any header fields as match keys, and you can define your own custom actions. Then you have your logical dataplane view.

## Slide 8: Protocol-Independent Switch Architecture (PISA)
Logical Data-plane View (your P4 program)
Switch Pipeline
Queues
Parser
Fixed Action
Match Table
Match Table
Match Table
Match Table
L2
IPv4
IPv6
ACL
Action Macro
Action Macro
Action Macro
Action Macro
Notes: So, let me give you quick overview of the PISA design.
Programmable parser. Packets run from left to right, going through each stage. Each stage offers generic, protocol-independent match-action units. You can use any header fields as match keys, and you can define your own custom actions. Then you have your logical dataplane view.

## Slide 9: Mapping to Physical Resources
Match Table
Action Macro
Queues
Parser
Match Table
Match Table
Match Table
L2 Table
IPv4 Table
IPv6 Table
ACL Table
Action Macro
Action Macro
Action Macro
L2
IPv4
IPv6
ACL
Logical Data-plane View (P4)
Switch Pipeline
L2
IPv6
ACL
IPv4
L2 Action Macro
v4 Action Macro
v6 Action
ACL Action Macro
packet
Notes: Compiler does the mapping between logical and physical tables.

## Slide 10: Re-configurability
Logical Data-plane View (P4)
Switch Pipeline
Queues
Parser
L2 Table
IPv4 Table
ACL Table
IPv6 Table
MyEncap
L2
IPv4
IPv6
ACL
MyEncap
L2 Action Macro
v4 Action Macro
ACL Action Macro
Action
MyEncap
v6 Action Macro
IPv4
Action
IPv4
Action
IPv6
Action
IPv6
Notes: - Adding my new forwarding function easy, since it comes before the forwarding tables, I make room for it and move v4 to stage 3
- Adding monitoring functions is easy too, I can add a monitoring action to any table
- Moving resources between functions is easy. If v6 was using even fewer entries I could reclaim that space for v4.

## Slide 11: P4: Three Goals
Protocol independence
  Define a packet parser
  Define a set of typed match+action tables
Target independence
  Program without knowledge of packet-processing device details
  Let compilers configure the target device
In-field Re-configurability
  Allow the users to change parsing and processing program in the field

## Slide 12: What does this mean?
To network device vendors
  S/W programming practices and tools used in every phase
  Extremely fast iteration and feature release
  Differentiation in capabilities and performance
  Can fix even data-plane bugs in the field
To large on-line service providers and carriers
  No more “black boxes” in the “white boxes”
  Your devs can program, test, and debug your network devices all the way down
  You keep your own ideas
You wear both hats 
Notes: program all the way down to how bits are shipped over the wire.
[1] Device vendors
- you’d be amazed to know how much much switch vendors spend to reimburse the damage caused by data-plane bugs in their customers’ networks.
[2] Large online service providers
Truly white box  even API is yours

## Slide 13: Key benefits of programmable forwarding
New features: Realize new protocols and behaviors very quickly
Reduce complexity: Remove unnecessary features and tables
Efficient use of H/W resources: Achieve biggest bang for buck
Greater visibility: New diagnostics, telemetry, OAM, etc.
Modularity: Compose forwarding behavior from libraries
Portability: Specify forwarding behavior once; compile to many devices
Own your own network: No need to wait for next chips or systems
Notes: Operations, Administration, and Maintenance (OAM): A group of network management functions that provide network fault indication, fault localization, performance information, and data and diagnosis functions.

## Slide 14: P4-Based Workflow
Parser
Match+Action Tables
Queues/ Scheduling
Packet Metadata
Device is not yet programmed
  Does not know about any packet formats or protocols

## Slide 15: P4-Based Workflow
Protocol
Authoring
1
Compile
2
Control
4
Parser
Match+Action Tables
Queues/ Scheduling
Packet Metadata
IPv4
IPv6
VLAN
Eth
Run-time API
Driver
Switch OS
Run!
5
L2_L3.p4
Load
3

## Slide 16: P4-Based Workflow
Protocol
Authoring
1
Compile
2
Control
4
Parser
Match+Action Tables
Queues/ Scheduling
Packet Metadata
IPv4
IPv6
VLAN
Eth
Run-time API
Driver
Switch OS
Run!
5
L2_L3.p4
Reconfigure
3
VXLAN.p4
UDP
VXLAN

## Slide 17: The P4 Language Consortium
Consortium of academic and industry members
Open source, evolving, domain-specific language
Permissive Apache license, code on GitHub today
Membership is free: contributions are welcome
Independent, set up as a California nonprofit

## Slide 18: P4.org Membership
Systems
Academia
Targets
Operators
Original P4 Paper Authors:
Open source, evolving, domain-specific language
Permissive Apache license, code on GitHub today
Membership is free: contributions are welcome
Independent, set up as a California nonprofit

## Slide 19: P4 Concepts
Pipeline
  Parser / Deparser
  Match-Action Tables

## Slide 20: The anatomy of a basic pipeline
Parser
  Converts packet data into a metadata (Parsed Representation)
Match+Action Tables
  Operate on metadata
Deparser
  Converts metadata back into a serialized packet
Metadata Bus
  Carries the information within the pipeline
All are optional
Metadata Bus

## Slide 21: Anatomy of a Switch
Ingress Pipeline
Egress Pipeline
Traffic Manager
  N:1 Relationships: Queueing, Congestion Control
  1:N Relationships: Replication
  Scheduling
Deparser
Metadata
Parser
Metadata
Queueing, Replication & Scheduling
Parser
Deparser
Metadata
Parser
Deparser
Metadata
Queueing, Replication & Scheduling

## Slide 22: Anatomy of a NIC
Single or Dual Pipeline
Parser
Deparser
Metadata
Deparser
Parser
Metadata
Network
Host

## Slide 23: Anatomy of Protocol Plugin
Single, “Bare” Pipeline
  No parsing/deparsing, just processing
Metadata
Input
Output

## Slide 24: P4 Program Sections
Parser
Deparser
Header / Metadata
parser parse_ethernet { extract(ethernet); return switch(ethernet.ethertype) { 0x8100 : parse_vlan_tag; 0x0800 : parse_ipv4; 0x8847 : parse_mpls; default: ingress; }
table port_table { … }
control ingress { apply(port_table); if (l2_meta.vlan_tags == 0) { process_assign_vlan();
} }
header_type ethernet_t { … }
header_type l2_metadata_t { … }
header ethernet_t ethernet;
header vlan_tag_t vlan_tag[2];
metadata l2_metadata_t l2_meta;
program.p4
Data Declarations
Parser Program
Table + Control Flow Program
P4 program defines what each table CAN do

## Slide 25: Control Plane Roles
Parser
Deparser
Header / Metadata
program.p4
P4 defined what each table CAN do
Queueing, Replication & Scheduling
...
Parser
Data Declarations
Parser Program
Table + Control Flow Program
Control plane or NOS decides switch runtime behavior
SDN controller or Network OS
match:action entries
queue, multicast, mirror configurations

## Slide 26: P4 & OpenFlow: Traditional SDN before P4
Fixed function data plane
Driver
OpenFlow Agent
OpenFlow Controller
Applications
Northbound API
OpenFlow Protocol

## Slide 27: P4 with OpenFlow
Data Plane
Driver
SBI Agent
Network Controller
Southbound API
Applications
Northbound API
Program
Compile
Target Binary
Auto-Generated API
User/Application Intent

## Slide 28: P4 with Network OS
Data Plane
Driver
Network OS (Linux, OPS, SONIC, FBOSS, ...)
Network Manager + central DB
Configuration API
(NOT per-flow)
Applications
Northbound API
Program
Compile
Target Binary
Auto-Generated API
User/Application Intent

## Slide 29: P4 Constructs
P4 Spec v1.0.2+
1.0.2: http://p4.org/wp-content/uploads/2015/04/p4-latest.pdf

## Slide 30: P4 Language Components
Data declarations
  Packet Headers and Metadata
Parser Programming
  Parser Functions (Parser states)
  Checksum Units
Packet Flow Programming
  Actions
    Primitive and compound actions
    Counters, Meters, Registers
  Tables
    Match keys
    Attributes
  Control Functions (Imperative Programs)
No: pointers, loops, recursion, floating point

## Slide 31: Headers and Fields (Packet)
Example: Declaring packet headers
header_type ethernet_t {
fields {
dstAddr : 48;
srcAddr : 48;
etherType : 16;
}
}
header_type vlan_tag_t {
fields {
pcp : 3;
cfi : 1;
vid : 12;
etherType : 16;
}
}
header ethernet_t ethernet;
header vlan_tag_t vlan_tag[3];
Actual Header Instantiation
Header Type Declarations
Handy Arrays for Header Stacks
Notes: Default data type is a “bitstring”, which can also be interpreted as an unsigned integer.
“signed” and “saturating” modifiers are also available

## Slide 32: Headers and Fields (Metadata)
Example: Declaring Metadata
header_type ingress_metadata_t {
fields {
/* Inputs */ ingress_port : 9; /* Available prior to parsing */
packet_length : 16; /* Might not be always available */
instance_type : 2; /* Normal, clone, recirculated */
ingress_global_tstamp : 48;
parser_status : 8; /* Parsing Error */
/* Outputs from Ingress Pipeline */
egress_spec : 16;
queue_id : 9;
}
}
metadata ingress_metadata_t ingress_metadata;
Actual Metadata Instantiation
Metadata is a header too

## Slide 33: Metadata vs. Packet Headers
Layout definition
  Packet header declarations define both the fields and the actual layout in the packet.
  Layout is not defined for metadata
Byte Alignment
  Packet header length must be a multiple of 8 bits
  No special requirements for metadata
Validity
  Packet headers are valid only if present in the packet
  Metadata is ALWAYS valid
    Default value is either 0 or can be specified explicitly
Acceptable fields
  Packet headers can contain calculated and variable length fields

## Slide 34: Variable-Length Fields
Example: Declaring IPv4 packet header
header_type ipv4_t {
fields {
version : 4;
ihl : 4;
diffserv : 8;
totalLen : 16;
identification : 16;
flags : 3;
fragOffset : 13;
ttl : 8;
protocol : 8;
hdrChecksum : 16;
srcAddr : 32;
dstAddr : 32;
options : *;
}
length : (ihl << 2);
max_length : 60;
}
Calculated, based on another field
Variable-length Field
Notes: While allowed by the spec, the current version of the compiler doesn’t support

## Slide 35: Defining a Parser Tree
Example: Simple Parser for L2/L3 Packets
header ethernet_t ethernet; header vlan_tag_t vlan_tag[2]; header ipv4_t ipv4; header ipv6_t ipv6;
parser start { extract(ethernet); return select(latest.etherType) { 0x8100, 0x9100 : parse_vlan_tag; 0x0800 : parse_ipv4; 0x86DD : parse_ipv6; default : ingress; } }
parser parse_vlan_tag { extract(vlan_tag[next]); return select(latest.etherType) {
0x8100 mask 0xEFFF : parse_vlan_tag; 0x0800 : parse_ipv4; 0x86DD : parse_ipv6; default : ingress; } }
Transitions to the next parser states.
Prioritized by order
This is not a reserved word, but a name of the Control Flow Function
IPv4
IPv6
VLAN
Eth
UDP
VXLAN
Notes: What do you think when a packet has more than 2 tags? – we will discuss parser exceptions 2 slides later

## Slide 36: Defining a Parser Tree (cont.)
Example: Simple Parser for L2/L3 Packets
header ethernet_t ethernet; header vlan_tag_t vlan_tag[2]; header ipv4_t ipv4; header ipv6_t ipv6;
parser start { extract(ethernet); return select(latest.etherType) { 0x8100, 0x9100 : parse_vlan_tag; 0x0800 : parse_ipv4; 0x86DD : parse_ipv6; default : ingress; } }
parser parse_vlan_tag { extract(vlan_tag[next]); return select(latest.etherType) {
0x8100 mask 0xEFFF : parse_vlan_tag; 0x0800 : parse_ipv4; 0x86DD : parse_ipv6; default : ingress; } }
parser parse_ipv4 { extract(ipv4); return ingress;
}
parser parse_ipv6 { extract(ipv6); return ingress; }
IPv4
IPv6
VLAN
Eth
UDP
VXLAN

## Slide 37: Parser Exceptions. Triggered implicitly or explicitly.
Example: Simple Parser for L2/L3 Packets
header ethernet_t ethernet; header vlan_tag_t vlan_tag[2]; header ipv4_t ipv4; header ipv6_t ipv6;
parser start { extract(ethernet); return select(latest.etherType) { 0x8100, 0x9100 : parse_vlan_tag; 0x0800 : parse_ipv4; 0x86DD : parse_ipv6; default : ingress; } }
parser parse_vlan_tag { extract(vlan_tag[next]); return select(latest.etherType) {
0x8100 mask 0xEFFF : parse_vlan_tag; 0x0800 : parse_ipv4; 0x86DD : parse_ipv6; default : ingress; } }
parser parse_ipv4 { extract(ipv4); return ingress;
}
parser parse_ipv6 { extract(ipv6); return ingress; }
parser_exception p4_pe_index_out_of_bounds { return ingress;
}
Standard exception, triggered when more than 2 VLAN tags.
Don’t parse after the second tag, but proceed as if it is an L2 packet

## Slide 38: Using Calculated Fields
Example: Calculated fields for IPv4
field_list ipv4_checksum_list { ipv4.version; ipv4.ihl; ipv4.diffserv; ipv4.totalLen; ipv4.identification; ipv4.flags; ipv4.fragOffset; ipv4.ttl; ipv4.protocol; ipv4.srcAddr; ipv4.dstAddr; }
field_list_calculation ipv4_checksum { input { ipv4_checksum_list; } algorithm : csum16; output_width : 16; }
calculated_field ipv4.hdrChecksum { verify ipv4_checksum; update ipv4_checksum; }
parser parse_ipv4 { extract(ipv4); return ingress; }
parser_exception p4_pe_checksum { return parser_drop;
}
Predefined parser state
Notes: “verify” is used by the parser
“update” is used by deparser

## Slide 39: Multi-field select statement
Example: Ipv4 Header Parsing
parser parse_ipv4 { extract(ipv4); set_metadata(ipv4_metadata.lkp_ipv4_sa, ipv4.srcAddr); set_metadata(ipv4_metadata.lkp_ipv4_da, ipv4.dstAddr); set_metadata(l3_metadata.lkp_ip_proto, ipv4.protocol); set_metadata(l3_metadata.lkp_ip_ttl, ipv4.ttl); return select(latest.fragOffset, latest.ihl, latest.protocol) { 0x0000501 : parse_icmp; 0x0000506 : parse_tcp; 0x0000511 : parse_udp; default : ingress;
}
Fields are joined for a match
Metadata can be initialized by the parser
Notes: In real programs, especially those that are designed to handle tunnels it is typical to have dedicated fields in the metadata for the “lookup” fields. For example if you have a tunneled packet, initially you’d place the outer L2/L3 addresses into the lookup fields. Later, if you decide to terminate the packet (and, thus, decap it), you’d copy the inner L2/L3 addresses into the lookup fields. At the same time, the lookup logic (dmac, ipv4/ipv6_fib) will always be the same and only “read” the dedicated lookup fields.

## Slide 40: Deparsing (Serializing packet headers)
Fundamental assumption of P4
  The device must be able to parse any packet it can produce
Consequence
  Packet headers can be reassembled using the parser definition
  When the device only need to insert a header but shouldn’t actually parse it
Example: insert my_header after udp
parser parse_udp { extract(udp); return select(latest.dst_port) { 0x0 mask 0x00 : ingress; default : parse_my_header;
}
Ingress parser will always transit to ingress
Parser tree has a branch to my_header for deparsing
Notes: Practical implication: If the parse tree mandates that VLAN tag must always precede IP header, the deparser will not be able to output a packet, where IP header precedes VLAN tag. If you want to be able to do such a rearrangement, then the parse tree should be written to be able to recognize it.

## Slide 41: P4 Language Components
Data declarations
Parser Programming
Packet Flow Programming
  Actions
    Primitive and compound actions
    Counters, Meters, Registers
  Tables
    Match keys
    Attributes
  Control Functions

## Slide 42: Actions
Primitive actions
  no_op, drop
  modify_field, modify_field_with_hash_based_offset
  add, add_to_field
  add_header, remove_header, copy_header
  push/pop (a header)
  count, execute_meter
  generate_digest
  truncate
  resubmit, recirculate, clone{_i2i, _e2i, _i2e, _e2e}
Compound actions
action route_ipv4(dst_port, dst_mac, src_mac, vid) { modify_field(standard_metadata.egress_spec, dst_port); modify_field(ethernet.dst_addr, dst_mac); modify_field(ethernet.src_addr, src_mac); modify_field(vlan_tag.vid, vid); add_to_field(ipv4.ttl, -1); }
Notes: Current support for expressions is limited. Older compilers might use primitive actions, like add(), subtract(), etc. Full support will appear in P4 v1.1

## Slide 43: Arithmetic and Logical Primitives
The current standard (v1.0.2)
  Primitive actions
    Standard: add(), add_to_field()
    Additional: subtract(), subtract_from_field(), bit_and(), bit_or(), bit_xor(), shift_left(), shift_right(), …
    add_to_field(ipv4.ttl, –1)
  Partial support for expressions exists in some compilers
Developing standard (p4-16)
  Expressions with +, -, &, |, ^, ~, <<, >>, etc.
    modify_field(ipv4.ttl, ipv4.ttl – 1)
  Specific targets might restrict expression complexity

## Slide 44: Action Execution Semantics
All actions within a compound action are assumed to be executed sequentially
action parallel_test() {
modify_field(hdr.fieldA, 1);
modify_field(hdr.fieldB, hdr.fieldA);
}
This is an important specification change
  Up to version 1.0.2 action execution was parallel
  After 1.0.2 action execution is sequential
The maximum number of steps supported for a compound action is target-dependent
 | Sequential Semantics | Parallel Semantics
fieldA | 1 | 1
fieldB | 1 | fieldA before action

## Slide 45: Match-Action Tables
The most fundamental units of the Match-Action Pipeline
P4 defines
  What to match on and match type
  A list of possible actions
  Additional attributes
    Size
In runtime, each table contains one or more entries (rows)
An entry contains:
  A specific key to match on
  A single action
    to be executed when a packet matches the entry
  (Optional) action data

## Slide 46: Example: IPv4 Processing
P4 Program
  Defines the format of the table
    Key Fields
    Actions
    Action Data
Control Plane (IP stack, Routing protocols)
  Populates table entries with specific information
    Based on the configuration
    Based on automatic discovery
    Based on protocol calculations
Data Plane (populated table)
  Performs the lookup
  Executes the chosen action
192.168.23.45
10.1.2.0/22
192.168.1.1
192.168.1.4
192.168.1.2
192.168.1.3
192.168.1.254
192.168.23.254
Key | Action | Action Data
192.168.1.1 | l3_switch | port= mac_da= mac_sa= vlan=
192.168.1.2 | l3_switch | port= mac_da= mac_sa= vlan=…
192.168.1.3 | l3_drop | 
192.168.1.254 | l3_l2_switch | port=
192.168.1.0/24 | l3_l2_switch | port=
10.1.2.0/22 | l3_switch_ecmp | ecmp_group=
Notes: This is one of the most important slides in the course, because it defines the responsibilities of the Data Plane vs. Control Plane. Many students have trouble separating these and waste a lot of time trying to figure out how does a P4 program populate table entries.

## Slide 47: Defining Actions
action l3_switch(port, mac_da, mac_sa, vlan) {
modify_field(metadata.egress_spec, port);
modify_field(ethernet.dstAddr, mac_da);
modify_field(ethernet.srcAddr, mac_sa);
modify_field(vlan_tag[0].vlanid, vlan);
modify_field(ipv4.ttl, ipv4.ttl – 1);
}
action l3_l2_switch(port) {
modify_field(metadata.egress_spec, port);
}
action l3_drop() {
drop();
}
action l3_switch_nexthop(nexthop_index) {
modify_field(l3_metadata.nexthop, nexthop_index);
modify_field(l3_metadata.nexthop_type, NEXTHOP_TYPE_SIMPLE);
}
action l3_switch_ecmp(ecmp_group) {
modify_field(l3_metadata.nexthop, ecmp_group);
modify_field(l3_metadata.nexthop_type, NEXTHOP_TYPE_ECMP);
}

## Slide 48: Match-Action Table (Exact Match)
Example: A typical L3 (IPv4) Host table
table ipv4_host { reads { ingress_metadata.vrf : exact; ipv4.dstAddr : exact; } actions { l3_switch; l3_l2_switch;
l3_switch_nexthop;
l3_switch_ecmp;
l3_drop;
} size : HOST_TABLE_SIZE; }
vrf | ipv4.dstAddr | action | data
1 | 192.168.1.10 | l3_switch | port_id= mac_da= mac_sa=
100 | 192.168.1.10 | l3_l2_switch | port_id=<CPU>
1 | 192.168.1.3 | l3_drop | 
5 | 10.10.1.1 | l3_switch_ecmp | ecmp_group=127
These are the only possible actions. Each particular entry can have only ONE of them.
Notes: virtual routing and forwarding (VRF)

## Slide 49: Match-Action Table (Longest Prefix Match)
Example: A typical L3 (IPv4) Routing table
table ipv4_lpm { reads { ingress_metadata.vrf : exact; ipv4.dstAddr : lpm; } actions { l3_l2_switch; l3_multicast; l3_nexthop; l3_ecmp; l3_drop; } size : 65536; }
vrf | ipv4.dstAddr / prefix | action | data
1 | 192.168.1.0 / 24 | l3_l2_switch | port_id=64
10 | 10.0.16.0 / 22 | l3_ecmp | ecmp_index=12
1 | 192.168.0.0 / 16 | l3_switch_nexthop | nexthop_index=451
1 | 0.0.0.0 / 0 | l3_switch_nexthop | nexthop_index=1
Prefix also serves as a priority indicator
Different fields can use different match types

## Slide 50: Match-Action Table (Ternary Match)
Example: A typical L3 (IPv4) Routing table
table ipv4_lpm { reads { ingress_metadata.vrf : ternary; ipv4.dstAddr : ternary; } actions { l3_l2_switch; l3_multicast; l3_nexthop; l3_ecmp; l3_drop; } size : 65536; }
Prio | vrf / mask | ipv4.dstAddr / mask | action | data
100 | 0x001/0xFFF | 192.168.1.5 / 255.255.255.255 | l3_swith_nexthop | nexthop_index=10
10 | 0x000/0x000 | 192.168.2.0/255.255.255.0 | l3_switch_ecmp | ecmp_index=25
10 | 0x000/0x000 | 192.168.3.0/255.255.255.0 | l3_switch_nexthop | nexthop_index=31
5 | 0x000/0x000 | 0.0.0.0/0.0.0.0 | l3_l2_switch | port_id=64
Ternary tables require an explicit specification of entry priority

## Slide 51: Match Types
Exact
  port_index : exact
Ternary
  ethernet.srcAddr : ternary
LPM (special kind of ternary match)
  ipv4.dstAddr : lpm
Range
  udp.dstPort : range
Valid
  vlan_tag[0] : valid

## Slide 52: Table Miss
Each table can have a Default Action
  Chosen by the Control Path at runtime from the list of table Actions
    P4 Program does not have an indication which action (and which action data) will be the default
When no matching entries are found
  Default Action with the default action data is executed if it has been set by the control path
  If no Default Action has been specified, it is no_op()

## Slide 53: Stateful Objects
Counters, Meters, Registers

## Slide 54: What are stateful objects
Stateful objects keep their state between packets
  Metadata and packet headers are stateless
    They are re-initialized for each packet
  Counters, Meters and Registers are stateful
    Counters are incremented with each packet
    Meters keep their bucket state
    Registers store arbitrary data

## Slide 55: Direct Counters
A counter per table entry
counter ip_acl_stats {
type : packets_and_bytes;
direct : ip_acl;
}
table ip_acl {
reads {
ipv4_metadata.lkp_ipv4_sa : ternary;
ipv4_metadata.lkp_ipv4_da : ternary;
l3_metadata.lkp_ip_proto : ternary;
l3_metadata.lkp_l4_sport : ternary;
l3_metadata.lkp_l4_dport : ternary;
}
actions {
nop;
acl_log;
acl_deny;
acl_permit;
acl_mirror;
acl_redirect_nexthop;
acl_redirect_ecmp;
}
size : INGRESS_IP_ACL_TABLE_SIZE;
}
matched entry
ABCD_xxxx_0123
BA8E_F007_xxxx
Match Fields
acl_permit
acl_deny
nop
Action Sel
8b
Action Data
pkt/byte counts
counter A
counter Z
Counter
8b
table ip_acl
counter ip_acl_stats

## Slide 56: Indirect Counters
Flexibly linked counters
counter ingress_bd_stats {
type : packets_and_bytes;
instance_count : BD_STATS_TABLE_SIZE;
}
action set_bd(bd, bd_stat_index) {
modify_field(l2_metadata.bd, bd);
count(ingress_bd_stats, bd_stat_index);
}
table port_vlan {
reads {
ingress_metadata.ingress_port : exact;
vlan_tag[0] : valid;
vlan_tag[0].vlan_id : exact;
}
actions {
set_bd;
}
}
Different VLANs (BDs) can share the same counter
matched entry
ABCD_0123
BA8E_F007
Match Fields
set_bd
set_bd
set_bd
set_bd
set_bd
set_bd
set_bd
Action Sel
bd
bd
bd
Action Data
table port_vlan
bd
bd
bd
bd
bd_stat_index
bd_stat_index A
bd_stat_index
bd_stat_index
bd_stat_index
bd_stat_index
bd_stat_index A
pkt/byte counts
counter ingress_bd_stats
Other tables can also reference these counters

## Slide 57: Meters
/* Direct Meter */
meter acl_meter {
type: packets;
direct: ip_acl;
result: metadata.color;
}
/* Indirect Meter Array */
meter bd_meter {
type: bytes;
instance_count: 1000;
}
action do_bd_meter(meter_index) {
execute_meter(bd_meter, meter_index, metadata.color);
}
Declaration is similar to counters
  Action: execute_meter(meter_array, meter_index, color_destination)
Meters calculate packet color and deposit it into the specified field
Color Coding:
0 – Green
1 – Yellow
2 -- Red

## Slide 58: Registers
  /* Register Array (Indirect) */
register last_syn {
width: 32;
static: flow_table;
instance_count: 1024;
}
action get_flow_age(flow_index) {
register_read(last_syn, flow_index, metadata.flow_start_time);
modify_field(metadata.flow_age,
metadata.flow_start_time – metadata.ingress_global_stamp);
}
action start_new_flow(flow_index) {
register_write(last_syn, flow_index, metadata.ingress_global_timestamp);
}
Declaration is similar to indirect counters
  Actions
    register_read(register_array, register_index, destination_field)
    register_write(register_array, register_index, value)

## Slide 59: Control Flow Functions
Primitives
  Perform a table lookup: apply
  if/else statement
  apply with the case clause
Sequential Execution Semantics
  Compiler is doing parallelization automatically
Standard control functions
  ingress() – Ingress Pipeline processing
  egress() – Egress Pipeline processing
User-defined control functions

## Slide 60: Standard Control Functions
control ingress {
apply(port_vlan_mapping);
apply(smac);
apply(dmac);
}
control egress {
apply(vlan_tag_removal);
}
ingress() control function starts processing
  remember “return ingress;” statement in the parser functions
egress() control function is called implicitly from the Packet Replication Engine

## Slide 61: User-Defined Control Functions
control assign_vlan {
apply(subnet_vlan);
apply(mac_vlan);
apply(protocol_vlan);
apply(port_vlan);
apply(resolve_vlan);
}
control ingress {
. . .
if (!valid(vlan_tag[0]) {
assign_vlan();
}
. . .
}
Help improve code readability
  No specific performance advantages: the code is flattened by the compiler
No parameters are accepted

## Slide 62: If/Else Branching
Example: Separate Ipv4 and IPv6 Processing Paths
if ((l3_metadata.lkp_ip_type == IPTYPE_IPV4) and (ipv4_metadata.ipv4_unicast_enabled == TRUE)) { process_ipv4_racl();
process_nat();
process_ipv4_urpf();
process_ipv4_fib();
} else {
if ((l3_metadata.lkp_ip_type == IPTYPE_IPV6) and (ipv6_metadata.ipv6_unicast_enabled == TRUE)) {
process_ipv6_racl();
process_ipv6_urpf();
process_ipv6_fib();
}
}

## Slide 63: Action Branching
Example: Use per-router-mac decapsulation
table router_mac { reads { l2_metadata.lkup_dst_mac : ternary;
l2_metadata.bd : ternary;
ingress_metadata.src_port: ternary;
}
actions {
nop;
enable_ipv4_lookup;
enable_ipv6_lookup;
enable_mpls_decap;
enable_mim_decap;
}
}
control process_router_mac_lookup { apply(router_mac) { enable_ipv4_lookup { process_ipv4_fib(); } enable_ipv6_lookup { process_ipv6_fib(); } enable_mpls_decap { process_mpls_label_lookup(); }
/* etc. */
} }

## Slide 64: Miss branching
action on_miss() {}
table ipv4_fib {
reads {
. . .
}
actions {
l3_switch;
l3_l2_switch;
l3_switch_nexthop;
l3_switch_ecmp;
on_miss;
}
}
control process_ipv4_fib { apply(ipv4_fib) { on_miss { apply(ipv4_fib_lpm); }
} }
We choose to use only this action as the default

## Slide 65: Executing actions in the control flow
control process_counters {
if (my_meta.drop_packet == 0) {
count(bd_counter, metadata.bd_counter_index);
count(vrf_counter, metadata.vrf_counter_index);
}
}
Actions cannot be directly referenced in the control flow functions
  Instead, they need to be “wrapped” into tables
Tables without keys can be used to implement unconditional execution
  They always miss and hence the desired action needs to be set as a default
action update_counters() {
count(bd_counter, metadata.bd_counter_index);
count(vrf_counter, metadata.vrf_counter_index);
}
table do_process_counters {
actions {
update_counters;
}
}
control process_counters {
if (my_meta.drop_packet == 0) {
apply(do_process_counters);
}
}
This action must be set as a default for this table by the control plane

## Slide 66: Advanced Concepts
Action Profiles
Packet Digests
Packet Resubmit/Recirculation
Packet Cloning

## Slide 67: Action Profiles
Separate table match entries from actions and action data
Allow multiple entries to share same action data
  Saves space
  Allows quick update of multiple entries
Allow multiple actions/action_data per entry
  This is called “dynamic action selection”
  Used to implement LAG or ECMP
Can be more efficient compared to explicit implementation

## Slide 68: Action Profiles
Actions can be complex
action set_bd(bd, vrf, rmac_group,
ipv4_unicast_enabled, ipv6_unicast_enabled,
ipv4_urpf_mode, ipv6_urpf_mode,
igmp_snooping_enabled, mld_snooping_enabled,
bd_label, stp_group, stats_idx,
exclusion_id)
{
modify_field(l3_metadata.vrf, vrf);
modify_field(ipv4_metadata.ipv4_unicast_enabled, ipv4_unicast_enabled);
modify_field(ipv6_metadata.ipv6_unicast_enabled, ipv6_unicast_enabled);
modify_field(ipv4_metadata.ipv4_urpf_mode, ipv4_urpf_mode);
modify_field(ipv6_metadata.ipv6_urpf_mode, ipv6_urpf_mode);
modify_field(l3_metadata.rmac_group, rmac_group);
modify_field(acl_metadata.bd_label, bd_label);
modify_field(ingress_metadata.bd, bd);
modify_field(ingress_metadata.outer_bd, bd);
modify_field(l2_metadata.stp_group, stp_group);
modify_field(l2_metadata.bd_stats_idx, stats_idx);
modify_field(multicast_metadata.igmp_snooping_enabled, igmp_snooping_enabled);
modify_field(multicast_metadata.mld_snooping_enabled, mld_snooping_enabled);
modify_field(ig_intr_md_for_tm.level1_exclusion_id, exclusion_id);
}
60-70 bits for the parameters

## Slide 69: Naïve implementation
Each entry has its own action, many entries do the same action – the table uses too much space
table port_vlan_mapping {
reads {
ingress_metadata.ifindex : exact;
vlan_tag[0] : valid;
vlan_tag[0].vid : exact;
vlan_tag[1] : valid;
vlan_tag[1].vid : exact;
}
actions {
set_bd;
set_bd_ipv4_mcast_switch_ipv6_mcast_switch_flags;
set_bd_ipv4_mcast_switch_ipv6_mcast_route_flags;
set_bd_ipv4_mcast_route_ipv6_mcast_switch_flags;
set_bd_ipv4_mcast_route_ipv6_mcast_route_flags;
}
size : 32768;
}
ABCD_0123
BA8E_F007
Match Fields
action A
action Z
Action Sel
Action Data
table port_vlan_mapping
32768
70 bit
~40 bit

## Slide 70: Manual Profile Implementation
Share the same action data bits with multiple entries
table port_vlan_mapping_profile {
reads {
metadata.profile_index : exact;
actions {
set_bd;
set_bd_ipv4_mcast_switch_ipv6_mcast_switch_flags;
set_bd_ipv4_mcast_switch_ipv6_mcast_route_flags;
set_bd_ipv4_mcast_route_ipv6_mcast_switch_flags;
set_bd_ipv4_mcast_route_ipv6_mcast_route_flags;
}
size : 8192;
}
action set_profile_index(index) {
modify_field(metadata.profile_index, index);
}
table port_vlan_mapping {
reads {
ingress_metadata.ifindex : exact;
vlan_tag[0] : valid;
vlan_tag[0].vid : exact;
vlan_tag[1] : valid;
vlan_tag[1].vid : exact;
}
actions {
set_profile_index;
}
size : 32768;
}
ABCD_0123
BA8E_F007
Match Fields
index
Action Profile
table port_vlan_mapping
action A
Action Sel
Action Data
action Z
table port_vlan_mapping_profile
32768
~40 bit
8192
80 bit
Notes: This method allows for some space savings, but introduces an explicit match dependency: matching in port_vlan_mapping_

## Slide 71: Using P4 profiles
Share the same action with multiple entries. Action profile can be shared by multiple tables too.
action_profile vlan_port_mapping_profile {
actions {
set_bd;
set_bd_ipv4_mcast_switch_ipv6_mcast_switch_flags;
set_bd_ipv4_mcast_switch_ipv6_mcast_route_flags;
set_bd_ipv4_mcast_route_ipv6_mcast_switch_flags;
set_bd_ipv4_mcast_route_ipv6_mcast_route_flags;
}
size : 8192;
}
table port_vlan_mapping {
reads {
ingress_metadata.ifindex : exact;
vlan_tag[0] : valid;
vlan_tag[0].vid : exact;
vlan_tag[1] : valid;
vlan_tag[1].vid : exact;
}
action_profile : vlan_port_mapping_profile;
size : 32768;
}
ABCD_0123
BA8E_F007
Match Fields
index
Action Profile
table port_vlan_mapping
action A
Action Sel
Action Data
action Z
action_profile vlan_port_mapping_profile
Notes: This is a more efficient implementation. One of the reasons: profile index is not explicitly exposed and can’t be accessed outside of this construct.

## Slide 72: Using the profiles for LAG and ECMP
action_selector ecmp_selector {
selection_key : ecmp_hash;
}
action_profile ecmp_action_profile {
actions {
nop;
set_ecmp_nexthop_details;
}
size : ECMP_SELECT_TABLE_SIZE;
dynamic_action_selection : ecmp_selector;
}
table ecmp_group {
reads {
l3_metadata.nexthop_index : exact;
}
action_profile: ecmp_action_profile;
size : ECMP_GROUP_TABLE_SIZE;
}
Chooses a GROUP of profile entries
Chooses a particular entry within a group

## Slide 73: Using the profiles for LAG and ECMP
action_selector ecmp_selector {
selection_key : ecmp_hash;
}
action_profile ecmp_action_profile {
actions {
nop;
set_ecmp_nexthop_details;
}
size : ECMP_SELECT_TABLE_SIZE;
dynamic_action_selection : ecmp_selector;
}
table ecmp_group {
reads {
l3_metadata.nexthop_index : exact;
}
action_profile: ecmp_action_profile;
size : ECMP_GROUP_TABLE_SIZE;
}
field_list l3_hash_fields {
ipv4_metadata.lkp_ipv4_sa;
ipv4_metadata.lkp_ipv4_da;
l3_metadata.lkp_ip_proto;
l3_metadata.lkp_l4_sport;
l3_metadata.lkp_l4_dport;
}
field_list_calculation ecmp_hash {
input {
l3_hash_fields;
}
algorithm : crc16;
output_width : ECMP_BIT_WIDTH;
}

## Slide 74: Packet Digests – Notify control plane of data plane events
Action
  generate_digest(receiver, field_list)
Sends the specified metadata to a target-specific receiver
  Software-based
  Hardware-Based

## Slide 75: Implementing MAC Learning
Source MAC Lookup
Learn Notification Generation
action smac_hit(src_port, static) {
modify_field(l2_metadata.src_port, src_port);
modify_field(l2_metadata.is_static, static);
modify_field(l2_metadata.src_move,
standard_metadata.igress_port ^ src_port);
}
action smac_miss() {
modify_field(l2_metadata.src_miss, TRUE);
}
table smac {
reads {
vlan_tag[0].vid : exact;
ethernet.srcAddr: exact;
}
actions {
smac_hit;
smac_miss;
}
}
field_list l2_learn_digest {
ethernet.srcAddr,
vlan_tag[0].vid,
standard_metadata.ingress_port,
l2_metadata.src_port,
l2_metadata.src_move
}
action send_learn_notification() {
generate_digest(L2_RECV, l2_learn_digest);
}
table learn_notification {
reads {
l2_metadata.src_move : exact;
l2_metadata.src_miss : exact;
l2_metadata.is_static: exact;
}
actions {
send_learn_notification;
}
}
control process_l2_learning {
apply(smac);
apply(learn_notification);
}
Target-specific number. Can be SW or HW receiver
Other fields can influence sending of learn notifications
Notes: L2_RECV is a number, appropriate for a given target. It can be a software or hardware receiver, that will be tasked with updating both SMAC and DMAC tables

## Slide 76: Resubmit and Recirculate
Implementing complex processing
resubmit(field_list)
  Unmodified packet is returned back to the parser within ingress pipeline, with additional metadata
  Useful for complex parsing
recirculate(field_list)
  Fully modified packet is returned back to the ingress parser after completing all the processing
  Useful for complex tunnel/NAT processing
standard_metadata.instance_type == PKT_INSTANCE_RESUBMIT
standard_metadata.instance_type == PKT_INSTANCE_RECIRCULATE
standard_metadata.instance_type == PKT_INSTANCE_NORMAL
Notes: For the P4 code it is typically important to be able to differentiate between the original and resubmit/recirculate copy. This is done using standard_metadata.instance_type field

## Slide 77: MPLS Processing (Simple)
parser parse_mpls {
extract(mpls[next]);
return select(latest.bos) {
0 : parse_mpls;
1 : parse_mpls_bos;
default : ingress;
}
}
parser parse_mpls_bos {
return select(current(0, 4)) {
0x4 : parse_inner_ipv4;
0x6 : parse_inner_ipv6;
default: parse_inner_ethernet;
}
}
This parser is a very effective hack
  MPLS does not formally carry any indication of the payload type
The right way to do parsing is by using label lookup

## Slide 78: MPLS Processing (Full)
Parser
Control Flow
#define IPV4 0
#define IPV6 1
#define ETHERNET 2
header_type my_metadata {
fields {
mpls_payload : 2;
}
}
parser parse_mpls_bos {
return select(
standard_metadata.resubmit_flag,
my_metadata.mpls_payload,
current(0, 4)) {
0x04 : parse_inner_ipv4;
0x06 : parse_inner_ipv6;
0x40 mask 0x70 : parse_inner_ipv4
0x50 mask 0x70 : parse_inner_ipv6;
0x60 mask 0x70 : parse_inner_ethernet;
default: parse_inner_ethernet;
}
}
action set_mpls_payload_type(mpls_payload) {
modify_field(my_metadata.mpls_payload, mpls_payload);
}
table mpls {
reads {
mpls[0].label : exact;
mpls[1].label : exact;
}
actions {
set_mpls_payload_type;
}
}
control ingress {
. . .
apply(mpls);
/* If our guess was wrong... */
if (my_metadata.mpls_payload == ETHERNET and !valid(inner_ethernet)) {
apply(mpls_resubmit);
}
. . .
}

## Slide 79: MPLS Processing (Resubmit)
field_list mpls_resubmit_list {
my_metadata.mpls_payload
}
action do_mpls_resubmit() {
resubmit(mpls_resubmit_list);
}
table mpls_resubmit {
actions {
do_mpls_resubmit;
}
}
The packet still goes through the rest of the ingress pipeline
  Use the if() statement around the rest of the code to avoid further processing
All metadata computed at the first pass will be lost
  Put all the fields that will be needed in the second pass into the resubmit field_list

## Slide 80: Cloning
A new copy of a packet is created
The original and the clone are processed independently
Two cloning sources
  Original packet (before ingress)
  Fully processed (after egress)
Two cloning destinations
  Beginning of the ingress pipeline
  Packet Queuing/Replication Engine
    Before the beginning of the egress pipeline
 | Packet before Ingress | Packet After Egress
Ingress Pipeline | clone_i2i() | clone_e2i()
Egress Pipeline | clone_i2e() | clone_e2e()
Source
Dest
clone_x2y(clone_spec, field_list)
Notes: As in the case of resubmit/recirculate, standard_metadata.instance_type provides values to distinguish between the original and the cloned copies.

## Slide 81: Implementing Negative Mirroring (aka mirror on drop)
Creating a mirrored copy
Processing the mirrored copy
field_list mirror_info {
i2e_metadata.mirror_session_id;
i2e_metadata.mirror_drop_flags;
}
action do_negative_mirror(session_id) {
modify_field(i2e_metadata.mirror_session_id, session_id);
modify_field(i2e_metadata.mirror_drop_flags,
ingress_metadata.drop_flags);
clone_i2e(session_id, mirror_info);
}
table negative_mirror {
actions {
do_negative_mirror;
}
}
control ingress {
. . .
if (ingress_metadata.drop_flags != 0) {
apply(negative_mirror);
}
}
action set_mirror_nhop(nhop_idx) {
modify_field(l3_metadata.nexthop_index, nhop_idx);
}
action set_mirror_bd(bd) {
modify_field(egress_metadata.bd, bd);
}
table mirror {
reads {
i2e_metadata.mirror_session_id : exact;
}
actions {
nop;
set_mirror_nhop;
set_mirror_bd;
}
size : MIRROR_SESSIONS_TABLE_SIZE;
}
control egress {
if (standard_metadata.instance_type == PKT_INSTANCE_TYPE_INGRESS_CLONE) {
apply(mirror);
else {
. . .
}
}

## Slide 82: P4 Compiler Overview

## Slide 83: Modular Compiler Overview
Single Front-End (p4-hlir)
  Translates P4 code into High-Level Intermediate Representation (HLIR)
    Similar to AST (Abstract Syntax Trees)
    Currently represented as a hierarchy of Python objects
    Frees backend developers from the burden of syntax analysis and target-independent semantic checks
    HLIR documentation is supplied with the frontend code
Multiple backends
  Code generators for various targets
    Software Switch Model (p4c-bm)
    Network Interface Cards
    Packet Processors / NPUs
    FPGAs, GPUs, ASICs
  Validators and graph generators
  Run-time API generators
Notes: PDF doc HLIRSpec

## Slide 84: P4 Modular Compiler
Control Flow & Parse Graphs
JSON config for bmv2, PD-lib
p4c-validate & p4c-graphs
Drivers
P4 Compiler
(p4-hlir)
Outputs
Backends
Frontend
p4c-bm
HLIR
Intermediate
Representation
p4c-hw-target
Device-specific config, PD-Lib
P4 program
Drivers

## Slide 85: Dependency Analysis

## Slide 86: Types of dependencies
Dependencies are inferred from target-independent P4 program analysis
Independent tables
Match Dependency
Action Dependency
Successor Dependency
Reverse Read Dependency

## Slide 87: Independent Tables
action ing_drop() {
modify_field(ing_metadata.drop, 1);
}
action set_egress_port(egress_port) {
modify_field(ing_metadata.egress_spec, egress_port);
}
table dmac {
reads {
ethernet.dstAddr : exact;
}
actions {
nop;
set_egress_port;
}
}
table smac_filter {
reads {
ethernet.srcAddr : exact;
}
actions {
nop;
ing_drop;
}
}
control ingress {
apply(dmac);
apply(smac_filter);
}
Tables are independent: both matching and action execution can be done in parallel
Parser
dmac
dmac
smac filter
smac filter

## Slide 88: Action Dependency
action ing_drop() {
modify_field(ing_metadata.drop, 1);
}
action set_egress_port(egress_port) {
modify_field(ing_metadata.egress_spec, egress_port);
}
table dmac {
reads {
ethernet.dstAddr : exact;
}
actions {
nop;
ing_drop;
set_egress_port;
}
}
table smac_filter {
reads {
ethernet.srcAddr : exact;
}
actions {
nop;
ing_drop;
}
}
control ingress {
apply(dmac);
apply(smac_filter);
}
Tables act on the same field and therefore must be placed in separate stages
Parser
dmac
dmac
smac filter
smac filter

## Slide 89: Match Dependency
action set_bd(bd) {
modify_field(ing_metadata.bd, bd);
}
table port_bd {
reads {
ing_metadata.ingress_port : exact;
}
actions {
set_bd;
}
}
table dmac {
reads {
ethernet.dstAddr : exact;
ing_metadata.bd : exact;
}
actions {
nop;
set_egress_port;
}
}
table smac_filter {
reads {
ethernet.srcAddr : exact;
}
actions {
nop;
ing_drop;
}
}
control ingress {
apply(port_bd);
apply(dmac);
apply(smac_filter);
}
The second table matches on the field, modified by the first.
Parser
dmac
dmac
smac filter
smac filter
port bd
port bd
smac filter
smac filter

## Slide 90: Successor Dependency
action set_bd(bd) {
modify_field(ing_metadata.bd, bd);
}
table port_bd {
reads {
ing_metadata.ingress_port : exact;
}
actions {
set_bd;
}
}
table dmac {
reads {
ethernet.dstAddr : exact;
ing_metadata.bd : exact;
}
actions {
nop;
ing_drop;
set_egress_port;
}
}
table smac_filter {
reads {
ethernet.srcAddr : exact;
}
actions {
nop;
ing_drop;
}
}
control ingress {
apply(port_bd);
if (ing_metadata.bd != 0) {
apply(dmac);
} else {
apply(smac_filter);
}
}
Only one of the tables will be matched for a given packet
Parser
dmac
dmac
smac filter
smac filter
port bd
port bd

## Slide 91: Reverse Read Dependency
action set_bd(bd) {
modify_field(ing_metadata.bd, bd);
}
table port_bd {
reads {
ing_metadata.ingress_port : exact;
}
actions {
set_bd;
}
}
table dmac {
reads {
ethernet.dstAddr : exact;
ing_metadata.bd : exact;
}
actions {
nop;
ing_drop;
set_egress_port;
}
}
table smac_mangle {
reads {
ethernet.srcAddr : exact;
}
actions {
nop;
set_bd;
}
}
control ingress {
apply(port_bd);
apply(dmac);
apply(smac_mangle);
}
The third table modifies a field used by the second table for matching. Therefore the action cannot take place before the second table matches.
Parser
dmac
dmac
smac mangle
smac mangle
port bd
port bd
smac mangle
smac mangle
Notes: Currently, swapping smac_mangle and dmac might result in a different placement.

## Slide 92: Automatic API Generation

## Slide 93: Network Device API Basics
Object Definitions (Schema)
  Reflects the object properties and methods
Object Relationships (Behavior)
  The quality of the API is directly dependent on how well the object relationships are specified

## Slide 94: P4 is an Ideal Base for a Network APIs
Clearly defined objects
  Tables
  Counters
  Meters
  Registers
Unambiguously defined relationships
  Control Flow Functions
Idea:
  Each of fundamental P4 objects has a “natural” schema

## Slide 95: Tables
Uniform representation
  Primary key: Entry ID
  Match Fields
  Action
  Action Data
    Depends on the action
Operations
  Entry Add
    (Match Fields, Action, Action Data)  Entry ID
  Entry Get
    (Entry ID)  (Match Fields, Action, Action Data)
  Entry Delete
    (Entry ID) 
  Entry Modify
    (Entry ID, Action, Action Data) 
  Entry Lookup
    (Match Fields, [Action, Action Data])  Entry ID
  Table Traverse
     [ EntryID0, EntryID1, … EntryIDn ]
  Table Default_Action Set
    (Action, Action Data) 
  Table Default_Action Get
     (Action, Action Data)
  Table Default Action Clear
    
Other Operations
  Table Size Get
  Table Occupancy Get
  Table Clear
ABCD_0123
BA8E_F007
Match Fields
action A
action Z
Action Sel
Action Data
EntryID

## Slide 96: Example API. Match & Action Specs
myprog.p4
pd_myprog.h
action a1(p11, p12) {…}
action a2(p21, p22, p23) {…}
action a3() {…}
table t1 {
reads {
meta.f1 : exact;
meta.f2 : ternary;
h1 : valid;
}
typedef struct p4_pd_myprog_a1_action_spec {
<type> p11;
<type> p12;
} p4_pd_myprog_a1_action_spec_t;
typedef struct p4_pd_myprog_a2_action_spec {
<type> p21;
<type> p22;
<type> p23;
} p4_pd_myprog_a2_action_spec_t;
typedef struct p4_pd_myprog_a3_action_spec {
} p4_pd_myprog_a3_action_spec_t;
typedef struct p4_pd_myprog_t1_match_spec {
<type> meta_f1;
<type> meta_f2;
<type> meta_f2_mask;
uint8_t h1_valid;
} p4_pd_myprog_t1_match_spec_t;
exact: f
ternary: f and f_mask
lpm: f and f_prefix_len
valid: f_valid
range: f_min and f_max

## Slide 97: Example API. Entry Add
myprog.p4
pd_myprog.h
action a1(p11, p12) {…}
action a2(p21, p22, p23) {…}
action a3() {…}
table t1 {
reads {
meta.f1 : exact;
meta.f2 : ternary;
h1 : valid;
}
actions {
a1;
a2;
a3;
}
}
p4_pd_status_t p4_pd_myprog_t1_entry_add_with_a1( p4_pd_target_t device_target,
p4_pd_session_t session_handle,
p4_pd_priority_t priority,
const p4_pd_myprog_t1_match_spec_t *match_spec,
const p4_pd_myprog_a1_action_spec_t *action_spec,
p4_pd_entry_handle_t *entry_hdl);
p4_pd_status_t p4_pd_myprog_t1_entry_add_with_a2( p4_pd_target_t device_target,
p4_pd_session_t session_handle,
p4_pd_priority_t priority,
const p4_pd_myprog_t1_match_spec_t *match_spec,
const p4_pd_myprog_a2_action_spec_t *action_spec,
p4_pd_entry_handle_t *entry_hdl);
p4_pd_status_t p4_pd_myprog_t1_entry_add_with_a3( p4_pd_target_t device_target,
p4_pd_session_t session_handle,
p4_pd_priority_t priority,
const p4_pd_myprog_t1_match_spec_t *match_spec,
const p4_pd_myprog_a3_action_spec_t *action_spec,
p4_pd_entry_handle_t *entry_hdl);

## Slide 98: Example API. Entry Modify
myprog.p4
pd_myprog.h
action a1(p11, p12) {…}
action a2(p21, p22, p23) {…}
action a3() {…}
table t1 {
reads {
meta.f1 : exact;
meta.f2 : ternary;
h1 : valid;
}
actions {
a1;
a2;
a3;
}
}
p4_pd_status_t p4_pd_myprog_t1_entry_modify_with_a1( p4_pd_target_t device_target,
p4_pd_session_t session_handle,
p4_pd_entry_handle_t entry_hdl,
const p4_pd_myprog_a1_action_spec_t *action_spec);
p4_pd_status_t p4_pd_myprog_t1_entry_modify_with_a2( p4_pd_target_t device_target,
p4_pd_session_t session_handle,
p4_pd_entry_handle_t entry_hdl,
const p4_pd_myprog_a2_action_spec_t *action_spec);
p4_pd_status_t p4_pd_myprog_t1_entry_modify_with_a3( p4_pd_target_t device_target,
p4_pd_session_t session_handle,
p4_pd_entry_handle_t entry_hdl,
const p4_pd_myprog_a3_action_spec_t *action_spec);

## Slide 99: Example API. Entry Delete and Lookup
myprog.p4
pd_myprog.h
action a1(p11, p12) {…}
action a2(p21, p22, p23) {…}
action a3() {…}
table t1 {
reads {
meta.f1 : exact;
meta.f2 : ternary;
h1 : valid;
}
actions {
a1;
a2;
a3;
}
}
p4_pd_status_t p4_pd_myprog_t1_entry_delete( p4_pd_target_t device_target,
p4_pd_session_t session_handle,
p4_pd_entry_handle_t entry_hdl);
p4_pd_status_t p4_pd_myprog_t1_entry_lookup(
p4_pd_target_t device_target,
p4_pd_session_t session_handle,
const p4_pd_myprog_t1_match_spec_t *match_spec,
p4_pd_entry_handle_t *entry_hdl);

## Slide 100: Example API. Entry Get
myprog.p4
pd_myprog.h
action a1(p11, p12) {…}
action a2(p21, p22, p23) {…}
action a3() {…}
table t1 {
reads {
meta.f1 : exact;
meta.f2 : ternary;
h1 : valid;
}
actions {
a1;
a2;
a3;
}
}
typedef enum {
P4_PD_MYPROG_ACTION_A1,
P4_PD_MYPROG_ACTION_A2,
P4_PD_MYPROG_ACTION_A3,
…
P4_PD_MYPROG_ACTION_COUNT;
} p4_pd_myprog_actions_t;
typedef union {
p4_pd_myprog_a1_action_spec_t a1;
p4_pd_myprog_a2_action_spec_t a2;
. . .
} p4_pd_myprog_action_spec_t;
p4_pd_status_t p4_pd_myprog_t1_entry_get( p4_pd_target_t device_target,
p4_pd_session_t session_handle,
p4_pd_entry_handle_t entry_hdl,
p4_pd_myprog_t1_match_spec_t *match_spec,
p4_pd_myprog_actions_t *action,
p4_pd_myprog_action_spec_t *action_spec_t);

## Slide 101: Example API. Default Action APIs
myprog.p4
pd_myprog.h
action a1(p11, p12) {…}
action a2(p21, p22, p23) {…}
action a3() {…}
table t1 {
reads {
meta.f1 : exact;
meta.f2 : ternary;
h1 : valid;
}
actions {
a1;
a2;
a3;
}
}
p4_pd_status_t p4_pd_myprog_t1_set_default_action_a1( p4_pd_target_t device_target,
p4_pd_session_t session_handle,
const p4_pd_myprog_a1_action_spec_t *action_spec);
p4_pd_status_t p4_pd_myprog_t1_set_default_action_a2( p4_pd_target_t device_target,
p4_pd_session_t session_handle,
const p4_pd_myprog_a2_action_spec_t *action_spec);
p4_pd_status_t p4_pd_myprog_t1_set_default_action_a3( p4_pd_target_t device_target,
p4_pd_session_t session_handle,
const p4_pd_myprog_a3_action_spec_t *action_spec);
p4_pd_status_t p4_pd_myprog_t1_clear_default_action( p4_pd_target_t device_target,
p4_pd_session_t session_handle);

## Slide 102: Counters
Individual Counter Operations
  Get
    (Counter Index or Entry ID)  Value
  Clear
    (Counter Index or Entry ID) 
  Set (optional)
    (Counter Index or Entry ID, Value) 
Counter Array Operations
  Width Get
  Array size Get
  Get All
  Clear All

## Slide 103: Example API
myprog.p4
pd_myprog.h
counter c1 {
type: packets_and_bytes;
direct: t1;
};
counter c2 {
type: bytes;
instance_count: 1000;
}
p4_pd_status_t p4_pd_myprog_c1_get( p4_pd_target_t device_target,
p4_pd_session_t session_handle,
p4_pd_entry_handle_t entry_hdl,
uint64_t *packets,
uint64_t *bytes);
p4_pd_status_t p4_pd_myprog_c2_get( p4_pd_target_t device_target,
p4_pd_session_t session_handle,
uint32_t counter_idx,
uint64_t *bytes);

## Slide 104: Meters
Individual Meter Operations
  Set
    (Meter Index or EntryID, Committed Rate, Committed Birst, Peak Rate, Peak Birst)
    Is that the only option?
    What about different meter types (color-blind/color-aware, single rate?)
      Are all meters in the array of the same type?
    Who standardizes the units (bits, bytes, kbits, Mbytes, etc.)?
    Who standardizes the colors?
  Get
    (Meter Index or Entry ID)  (Settings)

## Slide 105: Registers
Operations
  Set
    (Register Index or Entry ID, value) 
  Get
    (Register Index or Entry ID)  value
C type for the value depends on register definition
Optional Operations
  Width Get
  Get All
  Set All

## Slide 106: Discussion: Program-Dependent API style
Pros
  Easy to understand and use
  Some type checking
Cons
  N*3 + m functions per table
  Very inconvenient for CLI implementation

## Slide 107: Program-Dependent API style
myprog.p4
pd_myprog_style1.h
action a1(p11, p12) {…}
action a2(p21, p22, p23) {…}
action a3() {…}
table t1 {
reads {
meta.f1 : exact;
meta.f2 : ternary;
h1 : valid;
}
actions {
a1;
a2;
a3;
}
}
typedef enum {
P4_PD_MYPROG_ACTION__A1,
P4_PD_MYPROG_ACTION__A2,
. . .
P4_PD_MYPROG_ACTION__MAX
} p4_pd_myprog_actionid_t;
typedef enum {
P4_PD_MYPROG_TABLE__T1,
. . .
P4_PD_MYPROG_TABLE__MAX
} p4_pd_myprog_table_id_t;
typedef enum {
P4_PD_MYPROG_FIELD__META_F1,
P4_PD_MYPROG_FIELD__META_F2,
P4_PD_MYPROG_FIELD__META_F2__MASK,
P4_PD_MYPROG_FIELD__H1__VALID,
P4_PD_MYPROG_FIELD__P11,
P4_PD_MYPROG_FIELD__P12,
P4_PD_MYPROG_FIELD__P22,
P4_PD_MYPROG_FIELD__P23,
. . .
P4_MD_MYPROG_FIELD__MAX
} p4_pd_myprog_field_id_t;
Uniform structure and small number of P4 objects allow APIs to be generated automatically
Notes: In the current version of P4 match fields are bound to the tables at the declaration (i.e. declaration and instantiation are tied together). That’s why they are long, like meta_f1 and not just f1.

## Slide 108: Example API: Program-Independent style
myprog.p4
pi_myprog_style2.h
action a1(p11, p12) {…}
action a2(p21, p22, p23) {…}
action a3() {…}
table t1 {
reads {
meta.f1 : exact;
meta.f2 : ternary;
h1 : valid;
}
actions {
a1;
a2;
a3;
}
}
const char *p4_pi_action2str(
p4_pi_target_t program_indicator,
p4_pi_action_t action_id);
p4_pi_action_t p4_pi_str2action(
p4_pi_target_t program_indicator,
const char *action_str);
const char *p4_pi_table2str(
p4_pi_target_t program_indicator,
p4_pi_table_t table_id);
p4_pi_table_t p4_pi_str2table(
p4_pi_target_t program_indicator,
const char *table_str);
const char *p4_pi_field2str(
p4_pi_target_t program_indicator,
p4_pi_field_t field_id);
p4_pi_field_t p4_pi_str2field(
p4_pi_target_t program_indicator,
const char *field_str);

## Slide 109: Example API
myprog.p4
pi_myprog_style2.h
action a1(p11, p12) {…}
action a2(p21, p22, p23) {…}
action a3() {…}
table t1 {
reads {
meta.f1 : exact;
meta.f2 : ternary;
h1 : valid;
}
actions {
a1;
a2;
a3;
}
}
typedef struct {
. . .
} p4_pi_entry_t;
p4_pi_status_t p4_pi_entry_init(
p4_pi_target_t program_indicator,
p4_pi_table_t table_id,
p4_pi_entry_t *entry);
p4_pi_status_t p4_pi_entry_action_set(
p4_pi_entry_t *entry,
p4_pi_action_id_t action_id);
p4_pi_status_t p4_pi_entry_field_set(
p4_pi_entry_t *entry,
p4_pi_field_id_t field_id,
const void *value);
p4_pi_status_t p4_pi_entry_add(
p4_pi_target_t device_target,
p4_pi_session_handle_t session_hdl,
const p4_pi_entry_t *entry,
p4_pi_entry_id_t *entry_id);
Another Option:
struct p4_pi_value {
p4_pi_value_type_t type;
union {
uint8_t u8;
uint16_t u16;
uint32_t u32;
uint64_t u64;
. . .
}
}
Notes: p4_pi_table_id, p4_pi_action_id and p4_pi_field_id are just integers and thus can take p4_pd_<program>_{table,action,field}_id_t, which are enums and thus integers.
We can also have a system, where action is a field, but this creates complications, since action data fields are valid or invalid based on action.
An alternative for void *value would be a tagged generic value, like
struct p4_pi_value {
p4_pi_value_type_t type;
union {
uint8_t u8;
uint16_t u16;
uint32_t u32;
uint64_t u64;
. . .
}
}

## Slide 110: Example API
myprog.p4
pi_myprog_style2.h
action a1(p11, p12) {…}
action a2(p21, p22, p23) {…}
action a3() {…}
table t1 {
reads {
meta.f1 : exact;
meta.f2 : ternary;
h1 : valid;
}
actions {
a1;
a2;
a3;
}
}
p4_pi_status_t p4_pi_entry_add(
p4_pi_target_t device_target,
p4_pi_session_handle_t session_hdl,
const p4_pi_entry_t *entry,
p4_pi_entry_id_t *entry_id);
p4_pi_status_t p4_pi_entry_modify(
p4_pi_target_t device_target,
p4_pi_session_handle_t session_hdl,
p4_pi_entry_id_t entry_id
const p4_pi_entry_t *entry);
p4_pi_status_t p4_pi_entry_delete(
p4_pi_target_t device_target,
p4_pi_session_handle_t session_hdl,
p4_pi_entry_id_t entry_id);
p4_pi_status_t p4_pi_entry_get(
p4_pi_target_t device_target,
p4_pi_session_handle_t session_hdl,
p4_pi_entry_id_t entry_id
p4_pi_entry_t *entry);
p4_pi_status_t p4_pi_entry_lookup(
p4_pi_target_t device_target,
p4_pi_session_handle_t session_hdl,
const p4_pi_entry_t *entry,
p4_pi_entry_id_t *entry_id);

## Slide 111: Other APIs
Get a list of Tables defined for a target
Get a list of Actions for a Table
Get a list of applicable fields for a Table+Action
  Clearly separated in match fields and action data fields
Get Table Attributes (size, etc.)
Get Field Attributes (size, type, etc.)
. . .

## Slide 112: Discussion
Pros
  Extremely flexible and doesn’t depend on a program
  Implementation can be fully data driven
  P4 Program replacement possible
  Potentially, new tables/actions/fields can be added on the fly for incremental compilation
  Very Easy CLI and other tool implementation
Cons
  Almost no type checking
  More function calls required
    Separate calls to set each field

## Slide 113: API style
Uniform structure and small number of P4 objects allow APIs to be generated automatically
  In some cases, not all information can be derived
    P4 v.1.1 typing will help with action_spec
  P4 evolution need to include mechanisms to allow full, unambiguous API generation
Many API styles are possible
  API generators should be implemented as separate backends

## Slide 114: github.com/p4lang
switch.p4: reference p4 program
BMv2 (Behavioral Model v2): s/w switch runs p4
BMv2 compiler
supporting tools, scripts
Project summaries: link

## Slide 115: BMv2 Primitives
standard primitives https://github.com/p4lang/p4-hlir/blob/master/p4_hlir/frontend/primitives.json
bmv2 specific primitives https://github.com/p4lang/p4c-bm/blob/master/p4c_bm/primitives.json

## Slide 116: Intrinsic Metadata, provided by BMv2 switch
If one defines all these fields, all the simple_switch features will be supported, so it is recommended to define these fields in every program (to avoid a headache). header_type intrinsic_metadata_t { fields { ingress_global_timestamp : 48; // ingress timestamp, in microseconds mcast_grp : 4; // to be set in the ingress pipeline for multicast egress_rid : 4; // replication id, available on egress if packet was multicast mcast_hash : 16; // unused lf_field_list : 32; // set by generate_digest primitive, not to be used directly by P4 programmer resubmit_flag : 16; // used internally recirculate_flag : 16; // used internally } } metadata intrinsic_metadata_t intrinsic_metadata; header_type queueing_metadata_t { fields { enq_timestamp : 48; // in microseconds enq_qdepth : 16; deq_timedelta : 32; deq_qdepth : 16; } } metadata queueing_metadata_t queueing_metadata;

## Slide 117: Thank you

## Slide 118: History
2016-06-07: Version 4.1.1
  Minor edits to sync with P4-D2 version
2016-04-20: Version 4.1
  Restored missing section headers
  Minor cleanups
2016-04-15: Version 4.0
  Reformatted for 16:9
  Added Cloning section

## Slide 119: History
2016-04-01: Version 3.2
  Reformatted code sections using new “Code” templates
  Updated P4 Membership slide
  Added
2016-02-16: Version 3.1
  Better section divisions
  Moved Action profiles into the Advanced concepts section
  Added slides on wrapping actions in tables
  Fixed Minor Typos

## Slide 120: History
2015-11-20: Version 3.0
  Updated the language to pre 1.1 state
  Added more slides in the “Tables” section
  Added sections on Registers and Meters
  Completely replaced the slides on API generation
  Removed Barefoot-specific visualizations
  Reworked the animations in the introduction section and throughout
2015-10-27: Version 2.1
  Edits by Vladimir: New Section on P4 principles (unfinished)
2015-09-23: Version 2.0
  Edits by Jerry. New Template
2015-09-15: Version 1.2
  Edits by Vladimir. More Illustrations
2015-09-14: Version 1.1
  Edits by Jerry. Illustrations for Action Profiles
08/25/15: Initial Release